## Slide 1: GAT Price Financial Model: Key Assumptions
Virtual Focus Group Discussion with the Pre-Qualified Bidders
Mid-Merit Natural Gas Capacity Auction | ERC Case No. 2026-015 RM | Thursday, 22 October 2026
Notes: Good morning and welcome. I am [name] of the ERC. Today we walk you through the assumptions in the Commission's financial model for the Gas Auction Threshold Price. We will not show any prices today, only inputs, values and their basis. We want your views on whether these inputs are reasonable. Please hold questions until the discussion slots; use the chat for anything short.

## Slide 2: Why we are meeting today
Walk through the model inputs
Every parameter, its value and its basis or source.
Hear your evidence
Where do our values differ from current market terms? Tell us why, with documents.
No prices today
GAT Prices are issued only by Commission resolution, after this consultation.
Notes: Three things today. One, show you every assumption in the model and where it comes from. Two, hear from you where our values differ from what you see in the market, with evidence. Three, explain what happens next. To be clear: no GAT Price figures are shared today. Prices are set only by Commission resolution.

## Slide 3: How the model sets the GAT Price
CRF
Capital recovery: return of and on capital, financing, income and local taxes, G&A
+
OM
Fixed O&M and variable non-fuel O&M of the plant
=
GAT Price
PhP/kWh price ceiling for each Facility Type
Outside the GAT Price: Fuel Cost = Fuel Commodity Cost + Capped Landed Logistics Cost (CLLC), recovered through the Fuel Cost Pass-Through against the Gas Price Benchmark and caps.
Solved by iteration: equity NPV = 0 at the required equity return. Draft GAIR Secs. 8–9; DOE DC2026-06-0013 Sec. 7.2.
Notes: The model is a 30-year discounted cash-flow model of a reference plant. It finds the flat price per kWh at which equity earns exactly its required return. That price has two parts: CRF, the capital recovery for the plant, financing, taxes and overhead; and OM, the plant's fixed and variable operating cost. Fuel is outside. Gas commodity cost and the capped logistics cost, the CLLC, are paid through the Fuel Cost pass-through, against benchmarks and caps.

## Slide 4: Eleven reference cases, two dispatch views
DOE lot | Grid | Capacity | Technologies modelled | Delivery starts | Supply period (TOR)
Lot 1 – existing | Luzon | 1,400 MW | CCGT (3 × 466.7 MW) | 2026 | 5 yrs + 5 yrs extension
Lot 2 – existing | Luzon | 500 MW | CCGT (1 × 500 MW) | 2027 | 10 yrs
New-build | Luzon | 1,000 MW | CCGT, OCGT, gas engine | 2031 | 20 yrs
New-build | Visayas | 440 MW | CCGT, OCGT, gas engine | 2028 | 20 yrs
New-build | Visayas | 500 MW | CCGT, OCGT, gas engine | 2031 | 20 yrs
None | Mindanao | – | No Mindanao lot in the DOE TOR; not modelled | – | –
Case A – TOR view: capacity factor 42%, the top of every TOR band.
Case B – historical view: actual dispatch of the gas fleet, Jan 2024–Sep 2026.
Source: DOE Terms of Reference (Annex B), Secs. 1.1, 1.2, 4.2 and 18.3.
Notes: We model one reference plant for each DOE lot and technology: the two existing-plant lots in Luzon, and new-build CCGT, OCGT and gas-engine plants for Luzon and both Visayas lots. Each case is run twice: at the TOR capacity factor of 42 percent, and at the historical capacity factor of the gas fleet. The model works per kW, so plant size does not change the result.

## Slide 5: Plant size and dispatch
42%
Capacity factor, Case A
Top of the TOR band (37%–42%; Lot 1 38%–42%)
66.8% / 63.1%
Capacity factor, Case B
Existing fleet / whole fleet, Jan 2024–Sep 2026
0.2% / yr
Output degradation
Applied from COD (draft Annex A.20)
Parameter | Value | Basis / source
Lot 1 non-mid-merit energy | +24% capacity factor | TOR 4.2.2: paid Fuel Cost only, not the GAP
Capacity factor basis | Net (own use 0%, efficiency 100%) | Capacity factor already net of own use
Unit sizes | Lot split into equal units: CCGT 440–500 MW; OCGT 200–250 MW; gas engines 22–50 MW | Per-kW result is the same whatever the unit size
Case B source: MERALCO “Breakdown of Generation Charge” tables (plants supplying MERALCO), Jan 2024–Sep 2026.
Notes: Capacity factor drives energy, so it matters most. Case A uses 42 percent, the top of the TOR band. Case B uses what the gas fleet actually ran: 66.8 percent for existing plants and 63.1 percent for the whole fleet, from MERALCO's published generation-charge data. For Lot 1 we add 24 percent non-mid-merit energy, which the TOR pays at Fuel Cost only. Capacity factors are net, so no separate own-use deduction. Output degrades 0.2 percent a year.

## Slide 6: Construction, operation and base year
0
months to build
Existing CCGT (Lots 1, 2)
COD 2028
36
months to build
New CCGT
COD 2031
24
months to build
New OCGT
COD 2030
18
months to build
New gas engine
COD 2030
Parameter | Value | Basis / source
Operating (cost-recovery) period | 30 years from COD, all plants | ERC plant economic life (draft Annex A.8)
Base year for costs and FX | 2028 (real terms) | ERC model default
COD in the model | 2028 + construction period | Calendar year does not change a real-terms result; TOR delivery years apply
Notes: Existing plants have no construction period; their capital sits at year zero. New-build plants take 36 months for a CCGT, 24 for an OCGT and 18 for gas engines. Every plant recovers its costs over 30 years, the ERC economic-life basis, even where the TOR contract is shorter. The model base year is 2028.

## Slide 7: All-in project cost
US$600
Existing CCGT
per kW, Lots 1 and 2
US$1,500
New CCGT
per kW
US$1,375
New gas engine
per kW
US$875
New OCGT
per kW
Basis: current market levels plus 25% for turbine and EPC cost inflation (October 2026). Existing plants (navy, Lots 1 and 2) at an operational/retooled-plant value; new-build (green) the same for Luzon and Visayas. Costs are all-in and per kW of gross installed capacity (draft Annex A.3). The model calibrates equipment cost so the all-in total equals these targets.
Notes: This is the single biggest input. For existing plants we use 600 US dollars per kW. For new builds we use 1,500 for a CCGT, 1,375 for gas engines and 875 for an OCGT. These are current market levels plus 25 percent, reflecting turbine shortages and EPC cost inflation. All-in means equipment, balance of plant, transport, development, contingency, financing during construction, VAT, duties and initial working capital. If your recent quotes or financings say otherwise, this is the number we most want evidence on.

## Slide 8: What makes up the all-in cost
Item | Value | Basis / source
Balance of plant | 21% of equipment cost | ERC model default
Insurance, ocean freight, local transport | 4.5% of equipment cost | ERC model default
Development and other costs (land, permits) | 15% of EPC | ERC model default
Contingency | 4% of total cost | ERC model default
Initial working capital | 11.03% of EPC | ERC model default (draft Annex A.24)
Dedicated connection | 1 km line at US$40k/km; switchyard US$786k; 1 km road at US$182k/km | ERC model default; Associated Transmission Projects excluded (Sec. 9.3)
Major refurbishment | 5% of EPC in year 15 | ERC model default (draft Annex A.21)
Salvage value | 10%, received in the final year | Draft GAIR Sec. 8.3 (Annex A.23)
Notes: These are the percentages and fixed amounts the model uses to build up the all-in cost, plus two lifetime items: a major refurbishment of 5 percent of EPC in year 15, and a 10 percent salvage value at the end. Most are the ERC model defaults and are the same for every case.

## Slide 9: Operating and overhead costs
Technology | Fixed O&M (US$/kW-yr) | Variable non-fuel O&M (US$/MWh) | G&A
Existing CCGT (Lots 1, 2) | 13.71 | 2.00 | 6% of O&M
New CCGT (Luzon, Visayas) | 13.71 | 2.00 | 6% of O&M
New OCGT (Luzon, Visayas) | 8.50 | 4.50 | 6% of O&M
New gas engine (Luzon, Visayas) | 16.50 | 3.80 | 6% of O&M
Basis: ERC model O&M inputs; G&A at 6% of fixed plus variable O&M (corporate overhead standard, draft Annex A.6).
Excluded: fuel, and logistics (regasification, pipeline, storage). These are recovered through the Fuel Cost, within caps.
Notes: OM in the GAT Price is fixed O&M per kW per year plus variable non-fuel O&M per MWh. Logistics costs are not here: they moved to the Fuel Cost as the CLLC. G&A is 6 percent of O&M. We would welcome your long-term service agreement benchmarks on these values.

## Slide 10: Financing assumptions
70 : 30
Debt : equity
Project-finance standard (A.9)
8.0%
Cost of debt
Local and foreign, pre-tax (A.10)
15 yrs
Debt tenor
Local and foreign (A.11)
14.0%
Required equity return
Nominal; CAPM range 12%–14% (A.12)
Parameter | Value | Basis / source
Grace period ¦ debt service reserve | 6 months from COD ¦ 6 months | ERC model default (draft Annex A.25)
Upfront fees ¦ commitment fees | 2.0% ¦ 0.5% | ERC model default
Resulting WACC (reference only) | 9.8% (pre-tax 11.2%; after-tax 8.4%) | Model result, draft GAIR Sec. 8.8.8 check
Notes: Financing follows a standard project-finance structure: 70 percent debt, 30 percent equity. Debt costs 8 percent a year over 15 years, with a six-month grace period after COD and a six-month debt service reserve. Equity requires 14 percent nominal, within a CAPM range of 12 to 14 percent. The resulting WACC is shown for reference only.

## Slide 11: Taxes and incentives
Tax / charge | Value | Basis / source
Corporate income tax | 25%; no income tax holiday | CREATE Act; no BOI/PEZA incentive assumed (A.14)
Real property tax | 2% on 80% assessment level | Local Government Code (draft Sec. 8.8.3, A.26)
Local business tax | 1% | Local Government Code (draft Sec. 8.8.3)
ER 1-94 host-community benefit | PhP 0.03/kWh | DOE DC2025-10-0023 (draft Sec. 8.8.3)
VAT on imported equipment ¦ customs duty | 12%, not recovered ¦ 3% | NIRC Sec. 107; no BOI incentive, so VAT is a cost (A.22)
Withholding tax ¦ GRT ¦ documentary stamp tax | 10% ¦ 1% ¦ 0.5% | On interest and loan documents; NIRC
Notes: We assume no BOI or PEZA incentives and no income tax holiday, so corporate income tax is 25 percent from the start. Local taxes, the ER 1-94 host-community benefit, and taxes on financing are included in CRF. If you hold or expect incentives, tell us; we deliberately did not assume them.

## Slide 12: Exchange rate and inflation
PhP 62.756
per US$
BSP reference rate, 25 Sep 2026 (A.16)
0%
Annual escalation
Real terms; GAT Price not indexed (draft Sec. 8.9)
30 days
Working-capital cycle
Receivables, payables, inventory
The GAT Price and each Gas Auction Price are fixed in PhP/kWh for the term of the award, with no foreign-exchange indexation or pass-through (draft GAIR Sec. 8.5).
Notes: The model converts at 62.756 pesos per US dollar, the BSP reference rate on 25 September 2026. It runs in real terms with zero escalation, because the GAT Price is fixed in pesos and not indexed after award. Receivables, payables and inventory are 30 days.

## Slide 13: Complete parameter list
All 115 model parameters in nine groups: value, type and basis for each
Notes: Part two is the complete list: every parameter in the model's Inputs and Assumptions, 115 lines in nine groups, with its value and basis. We will move quickly; the slides are yours to keep and check line by line. Flag anything you want to discuss.

## Slide 14: How to read the parameter tables
Column | What it shows
Parameter | Model line item, with its unit and the draft Annex A item where one applies
Type | How the value is set (colour key below)
Case | A (teal) = TOR capacity factor; B (purple) = historical; “A = B” when both give the same value
Lot 1 … gas engine | Value for each Luzon case; headers coloured by lot (Visayas on its own slides)
Basis / source | Where the value comes from
Input
Typed into the model; open for comment
Calculated
Follows from the inputs
Calibrated
Solved so the all-in cost equals its target
Notes: Quick guide to the tables. Values are for the Luzon cases at the TOR capacity factor, Case A. Where the historical-dispatch case, Case B, gives a different value, it gets its own purple line under the teal Case A line. Visayas cases use the same per-kW inputs at 440 or 500 megawatts. Where all five cases share one value, it is shown once across the row. The Type column says whether a value is typed in, calculated, or calibrated.

## Slide 15: Colour key: cases, lots and regions
A
Case A – TOR capacity factor
42% for every case
B
Case B – historical capacity factor
66.8% Lots 1–2; 63.1% new-build
Lot 1 – existing, Luzon
Lot 2 – existing, Luzon
New-build – Luzon
New-build – Visayas 440 MW
New-build – Visayas 500 MW
Mindanao – no lot in the DOE TOR
Notes: The same colours run through every slide. Teal is Case A, the TOR capacity factor; purple is Case B, the historical one. Each lot and region has its own colour: navy for Lot 1, blue for Lot 2, green for new-build Luzon, orange for Visayas 440 megawatts and magenta for Visayas 500 megawatts. Mindanao is grey: the DOE TOR has no Mindanao lot, so it is not modelled.

## Slide 16: 1. Plant and dispatch (1 of 2)
Parameter | Type | Case | Lot 1 existing | Lot 2 existing | New CCGT | New OCGT | New gas engine | Basis / source
Unit Capacity of Plant (MW/unit) | Input | A = B | 466.7 | 500 | 500 | 200 | 50 | TOR lot size split into equal units (at most 20 per case); the result is per kW, so unit size does not change it
No. of Units (unit) | Input | A = B | 3 | 1 | 2 | 5 | 20 | TOR auction capacity (Sec. 1.1) ÷ unit size
Installed Capacity, gross (MW) (Annex A.1) | Calculated | A = B | 1,400 | 500 | 1,000 | 1,000 | 1,000 | TOR Sec. 1.1 auction capacity requirement
Net Capacity Factor input (availability x dispatch) (Annex A.2) | Input | A | All cases: 42% |  |  |  |  | Case A: 42%, top of the TOR band. Case B: MERALCO-supplier gas fleet, Jan 2024–Sep 2026 (also applied to Visayas)
 |  | B | 66.8% | 66.8% | 63.12% | 63.12% | 63.12% | 
Guaranteed Efficiency Factor, % | Input | A = B | All cases: 100% |  |  |  |  | Net basis: capacity factor is already net
Notes: Plant size and dispatch. Capacity comes from the TOR lot sizes, split into standard units. Capacity factor is 42 percent in Case A, teal; Case B, purple, sits on the line below. Everything is on a net basis, and output degrades 0.2 percent a year.

## Slide 17: 1. Plant and dispatch (2 of 2)
Parameter | Type | Case | Lot 1 existing | Lot 2 existing | New CCGT | New OCGT | New gas engine | Basis / source
Allowance for losses & own use, % | Input | A = B | All cases: 0% |  |  |  |  | Net basis: capacity factor is net of own use
Net Capacity Factor after own use (calculated) (Annex A.2) | Calculated | A | All cases: 42% |  |  |  |  | Calculated by the model
 |  | B | 66.8% | 66.8% | 63.12% | 63.12% | 63.12% | 
Hours per Year (hours) | Calculated | A = B | All cases: 8,760 |  |  |  |  | Calculated by the model
Net Electrical Output (GWh, first year) | Calculated | A | 5,150.9 | 1,839.6 | 3,679.2 | 3,679.2 | 3,679.2 | Installed MW × capacity factor × 8,760 h
 |  | B | 8,192.4 | 2,925.9 | 5,529.7 | 5,529.7 | 5,529.7 | 
Plant Degradation Rate, % p.a. (Annex A.20) | Input | A = B | All cases: 0.2% |  |  |  |  | Draft Annex A.20
Heat rate (logistics only; fuel excluded) (Btu/kWh) | Input | A = B | 6,350 | 6,350 | 6,100 | 9,800 | 8,000 | Technology reference values; used only for logistics, which is now in the Fuel Cost: no effect on the GAT Price
Notes: Continuing this group. Same layout: the value for each case, then the basis. I will pause on any line you flag.

## Slide 18: 2. Timing (1 of 2)
Parameter | Type | Case | Lot 1 existing | Lot 2 existing | New CCGT | New OCGT | New gas engine | Basis / source
Construction Period (mos) (Annex A.7) | Input | A = B | 0 | 0 | 36 | 24 | 18 | Typical EPC schedule by technology (Annex A.7); existing plants have none
Operating Period (yrs from COD) (Annex A.8) | Input | A = B | All cases: 30 |  |  |  |  | ERC plant economic life for cost recovery, although the TOR contract is shorter (Annex A.8)
Yrs from base year CPI & Forex (2028) for FIT (years) | Calculated | A = B | 0 | 0 | 3 | 2 | 2 | Calculated by the model
Yrs from base year CPI (2028) for CAPEX (years) | Input | A = B | All cases: 0 |  |  |  |  | ERC model default
Notes: Timing. Construction runs zero to 36 months by technology, recovery is over 30 years, and all costs are in 2028 terms, so there is no escalation offset to worry about.

## Slide 19: 2. Timing (2 of 2)
Parameter | Type | Case | Lot 1 existing | Lot 2 existing | New CCGT | New OCGT | New gas engine | Basis / source
Yrs from base year CPI (2028) for OPEX (years) | Input | A = B | All cases: 0 |  |  |  |  | ERC model default
Base year CPI & Forex for FiT | Input | A = B | All cases: 2028 |  |  |  |  | ERC model default
Base year CPI for CAPEX | Input | A = B | All cases: 2028 |  |  |  |  | ERC model default
Base year CPI for OPEX | Input | A = B | All cases: 2028 |  |  |  |  | ERC model default
Commercial Operating Date (year) | Calculated | A = B | 2028 | 2028 | 2031 | 2030 | 2030 | Model base year 2028 plus construction; real terms, so the calendar year does not change the result. TOR delivery years apply in the auction
Notes: Continuing this group. Same layout: the value for each case, then the basis. I will pause on any line you flag.

## Slide 20: 3. Capital cost (1 of 3)
Parameter | Type | Case | Lot 1 existing | Lot 2 existing | New CCGT | New OCGT | New gas engine | Basis / source
Target all-in project cost (US$/kW) (Annex A.3) | Input | A = B | 600 | 600 | 1,500 | 875 | 1,375 | Current market levels +25% for turbine and EPC inflation (Oct 2026); existing plants at an operational/retooled-plant value (Annex A.3)
All-In Project Cost (Annex A.3) (US$/kW) | Calculated | A = B | 600 | 600 | 1,500 | 875 | 1,375 | Model result; equals the target
EPC Cost (US$/kW) | Calculated | A = B | 414.5 | 413.5 | 947.5 | 569.3 | 908.4 | Calculated by the model
Plant Cost (Excluding VAT, Financing, Working Capital) (US$/kW) | Calculated | A = B | 507.5 | 507.6 | 1,159 | 697 | 1,112 | Calculated by the model
Land cost, $000 | Calculated | A = B | All cases: 79.67 |  |  |  |  | Calculated by the model
Equipment Cost ex BOP, Transport ($000/MW) | Calibrated | A = B | 330 | 329 | 755 | 454 | 724 | Set by model calibration so the all-in cost equals the target
Notes: Capital cost. The all-in cost targets drive everything here; the model calibrates equipment cost to hit them. The percentages for balance of plant, freight, development, contingency and working capital are model defaults we invite you to test.

## Slide 21: 3. Capital cost (2 of 3)
Parameter | Type | Case | Lot 1 existing | Lot 2 existing | New CCGT | New OCGT | New gas engine | Basis / source
Insurance, Ocean Freight, Local Transport, % of Equipment Cost | Input | A = B | All cases: 4.5% |  |  |  |  | ERC model default
Balance of Plant (BOP), % of Equipment Cost | Input | A = B | All cases: 21% |  |  |  |  | ERC model default
Transmission Line Distance (km) | Input | A = B | All cases: 1 |  |  |  |  | Dedicated connection only; Associated Transmission Projects excluded (draft GAIR Sec. 9.3)
T/L Cost per km, 69 kV ($000/km) | Input | A = B | All cases: 40 |  |  |  |  | ERC model default; dedicated connection only (Sec. 9.3)
Switchyard & Transformers ($000) | Input | A = B | All cases: 786 |  |  |  |  | ERC model default; dedicated connection only (Sec. 9.3)
Access Roads ($000/km) | Input | A = B | All cases: 182 |  |  |  |  | ERC model default
Distance of Access Road (km) | Input | A = B | All cases: 1 |  |  |  |  | ERC model default
Dev't & Other Costs (land, permits, etc) (% of EPC) | Input | A = B | All cases: 15% |  |  |  |  | ERC model default
Notes: Continuing this group. Same layout: the value for each case, then the basis. I will pause on any line you flag.

## Slide 22: 3. Capital cost (3 of 3)
Parameter | Type | Case | Lot 1 existing | Lot 2 existing | New CCGT | New OCGT | New gas engine | Basis / source
VAT on importation (Annex A.22) | Calculated | A = B | All cases: 12% |  |  |  |  | 12% VAT (NIRC Sec. 107); not recovered without a BOI incentive, so it is a project cost (Annex A.22)
Customs Duty (Annex A.22) | Calculated | A = B | All cases: 3% |  |  |  |  | ERC model default (Annex A.22)
Initial Working Capital (% of EPC) (Annex A.24) | Input | A = B | All cases: 11.03% |  |  |  |  | ERC model default (Annex A.24)
Contingency (% of Total Cost) | Input | A = B | All cases: 4% |  |  |  |  | ERC model default
Salvage Value, % (Annex A.23) | Input | A = B | All cases: 10% |  |  |  |  | 10% of cost, received in the final year (draft GAIR Sec. 8.3; Annex A.23)
Major Maintenance/Refurbishment (% of EPC) (Annex A.21) | Input | A = B | All cases: 5% |  |  |  |  | ERC model default (Annex A.21)
Timing of Refurbishment (yr from COD) (Annex A.21) | Input | A = B | All cases: 15 |  |  |  |  | ERC model default (Annex A.21)
Notes: Continuing this group. Same layout: the value for each case, then the basis. I will pause on any line you flag.

## Slide 23: 4. Uses and sources of funds (1 of 2)
Parameter | Type | Case | Lot 1 existing | Lot 2 existing | New CCGT | New OCGT | New gas engine | Basis / source
Land Cost (US$ million) | Calculated | A = B | All cases: 0.08 |  |  |  |  | Calculated by the model
EPC (Equipment, Balance of Plant, Transport) (US$ million) | Calculated | A = B | 580.4 | 206.8 | 947.5 | 569.3 | 908.4 | Calculated by the model
Transmission Line Interconnection Facility (US$ million) | Calculated | A = B | All cases: 0.04 |  |  |  |  | Calculated by the model
Sub-Station Facility (US$ million) | Calculated | A = B | All cases: 0.79 |  |  |  |  | Calculated by the model
Development & Other Costs (Civil Works, Customs Duty) (US$ million) | Calculated | A = B | 102.6 | 36.7 | 167.4 | 100.7 | 160.5 | Calculated by the model
Construction Contingency (US$ million) | Calculated | A = B | 26.7 | 9.6 | 43.6 | 26.2 | 41.8 | Calculated by the model
Notes: Uses and sources of funds, in US dollar millions. These follow from the all-in cost and the 70-30 capital structure. Financing cost during construction is largest for the CCGT because it takes three years to build.

## Slide 24: 4. Uses and sources of funds (2 of 2)
Parameter | Type | Case | Lot 1 existing | Lot 2 existing | New CCGT | New OCGT | New gas engine | Basis / source
Value Added Tax (US$ million) | Calculated | A = B | 50.5 | 18.0 | 82.5 | 49.6 | 79.1 | Calculated by the model
Financing Costs (US$ million) | Calculated | A = B | 14.8 | 5.3 | 153.5 | 65.5 | 84.1 | Calculated by the model
Initial Working Capital (US$ million) | Calculated | A = B | 64.0 | 22.8 | 104.5 | 62.8 | 100.2 | Calculated by the model
Total Uses of Fund (US$ million) | Calculated | A = B | 840.0 | 300.0 | 1,500.0 | 875.0 | 1,375.0 | Calculated by the model
Debt (US$ million) | Calculated | A = B | 588.0 | 210.0 | 1,050.0 | 612.5 | 962.5 | Calculated by the model
Equity (US$ million) | Calculated | A = B | 252.0 | 90.0 | 450.0 | 262.5 | 412.5 | Calculated by the model
Total Sources of Fund (US$ million) | Calculated | A = B | 840.0 | 300.0 | 1,500.0 | 875.0 | 1,375.0 | Calculated by the model
Notes: Continuing this group. Same layout: the value for each case, then the basis. I will pause on any line you flag.

## Slide 25: 5. O&M and G&A (1 of 2)
Parameter | Type | Case | Lot 1 existing | Lot 2 existing | New CCGT | New OCGT | New gas engine | Basis / source
Fixed O&M Costs ($000/unit/year) (Annex A.4) | Input | A = B | 6,398 | 6,855 | 6,855 | 1,700 | 825 | Fixed O&M (US$/kW-yr) × unit MW: CCGT 13.71, OCGT 8.50, gas engine 16.50
Variable Non-Fuel O&M, excl. logistics ($000/MW/yr) (Annex A.5) | Input | A | 11.56 | 7.36 | 7.36 | 16.56 | 13.98 | Variable O&M × 8,760 × energy CF ÷ 1,000; US$2.00/MWh CCGT, 4.50 OCGT, 3.80 gas engine; logistics excluded
 |  | B | 11.7 | 11.7 | 11.06 | 24.88 | 21.01 | 
G&A Costs ($000/year) (Annex A.6) | Input | A | 2,123 | 632 | 1,264 | 1,503 | 1,829 | 6% of fixed + variable O&M (corporate overhead standard, Annex A.6)
 |  | B | 2,135 | 762 | 1,486 | 2,003 | 2,251 | 
Notes: O&M and G&A. Fixed O&M per kW-year, variable non-fuel O&M per MWh, and G&A at 6 percent. Logistics are excluded. The three target lines are reference values only and do not enter the calculation.

## Slide 26: 5. O&M and G&A (2 of 2)
Parameter | Type | Case | Lot 1 existing | Lot 2 existing | New CCGT | New OCGT | New gas engine | Basis / source
O&M + Spares as % of EPC, T/L, S/S | Calculated | A | 6.09% | 5.07% | 2.22% | 4.39% | 3.35% | Calculated by the model
 |  | B | 6.12% | 6.12% | 2.61% | 5.86% | 4.13% | 
Target fixed O&M (US$/kW-yr) (Annex A.4) - reference only | Input | A = B | 18 | 18 | 45 | 26.25 | 41.25 | Reference only; not used in the calculation
Target variable O&M (US$/MWh) (Annex A.5) - reference only | Input | A | 1.631 | 1.631 | 4.077 | 2.378 | 3.737 | Reference only; not used in the calculation
 |  | B | 1.025 | 1.025 | 2.713 | 1.582 | 2.487 | 
Target G&A (US$000/yr) (Annex A.6) - reference only | Input | A = B | All cases: 53.86 |  |  |  |  | Reference only; not used in the calculation
Notes: Continuing this group. Same layout: the value for each case, then the basis. I will pause on any line you flag.

## Slide 27: 6. Financing (1 of 2)
Parameter | Type | Case | Lot 1 existing | Lot 2 existing | New CCGT | New OCGT | New gas engine | Basis / source
Debt Ratio (Annex A.9) | Input | A = B | All cases: 70% |  |  |  |  | 70:30, commercial project-finance standard (Annex A.9)
Equity Ratio (Annex A.9) | Calculated | A = B | All cases: 30% |  |  |  |  | Calculated by the model
Local Capital | Calculated | A = B | 48.96% | 49.08% | 48.93% | 48.96% | 48.93% | Calculated by the model
Foreign Capital | Calculated | A = B | 51.04% | 50.92% | 51.07% | 51.04% | 51.07% | Calculated by the model
Cost of Debt, local (% excl. tax) (Annex A.10) | Input | A = B | All cases: 8% |  |  |  |  | 8% pre-tax (Annex A.10); local about 7.5%, US$ about 8.5%
Cost of Debt, foreign (% excl. tax) (Annex A.10) | Input | A = B | All cases: 8% |  |  |  |  | Same as local (Annex A.10)
Local Debt Repayment Period (yrs) (Annex A.11) | Input | A = B | All cases: 15 |  |  |  |  | 15 years (Annex A.11)
Foreign Debt Repayment Period (yrs) (Annex A.11) | Input | A = B | All cases: 15 |  |  |  |  | 15 years (Annex A.11)
Debt Grace Period from COD (mos) (Annex A.25) | Input | A = B | All cases: 6 |  |  |  |  | ERC model default (Annex A.25)
Local and Foreign debt Service Reserve (mos) | Input | A = B | All cases: 6 |  |  |  |  | ERC model default
Notes: Financing. 70-30 debt to equity, 8 percent debt over 15 years with a six-month grace, 14 percent equity return. The local and foreign split and the debt amounts are calculated. WACC is a result, shown for reference.

## Slide 28: 6. Financing (2 of 2)
Parameter | Type | Case | Lot 1 existing | Lot 2 existing | New CCGT | New OCGT | New gas engine | Basis / source
Local & Foreign Upfront & Financing Fees | Input | A = B | All cases: 2% |  |  |  |  | ERC model default
Local & Foreign Commitment Fees | Input | A = B | All cases: 0.5% |  |  |  |  | ERC model default
Total Local Debt (US$ million) | Calculated | A = B | 159.2 | 57.2 | 284.0 | 165.9 | 260.3 | Calculated by the model
Total Foreign Debt (US$ million) | Calculated | A = B | 428.8 | 152.8 | 766.0 | 446.6 | 702.2 | Calculated by the model
Total Debt Amount (US$ million) | Calculated | A = B | 588.0 | 210.0 | 1,050.0 | 612.5 | 962.5 | Calculated by the model
Equity Investment (US$ million) | Calculated | A = B | 252.0 | 90.0 | 450.0 | 262.5 | 412.5 | Calculated by the model
Required Equity Return, Re (nominal) (Annex A.12) (% p.a.) | Input | A = B | All cases: 14% |  |  |  |  | 14% nominal; CAPM range 12%–14% (Annex A.12)
WACC pre-tax | Calculated | A = B | All cases: 11.2% |  |  |  |  | Model result; reference check (draft GAIR Sec. 8.8.8)
WACC after-tax | Calculated | A = B | All cases: 8.4% |  |  |  |  | Calculated by the model
WACC | Calculated | A = B | All cases: 9.8% |  |  |  |  | Calculated by the model
Notes: Continuing this group. Same layout: the value for each case, then the basis. I will pause on any line you flag.

## Slide 29: 7. Taxes and incentives (1 of 2)
Parameter | Type | Case | Lot 1 existing | Lot 2 existing | New CCGT | New OCGT | New gas engine | Basis / source
Type of incentives (1 = NO, 2 = BOI, 3 = PEZA) | Input | A = B | All cases: 1 |  |  |  |  | No BOI or PEZA incentive assumed
Income Tax Holiday (yrs) (Annex A.14) | Calculated | A = B | All cases: 0 |  |  |  |  | None assumed (Annex A.14)
Income Tax Rate (after ITH) (Annex A.14) | Calculated | A = B | All cases: 25% |  |  |  |  | Corporate income tax, CREATE Act (Annex A.14)
Real Property Tax (from COD) (Sec. 8.8.3) | Calculated | A = B | All cases: 2% |  |  |  |  | Local Government Code (draft GAIR Sec. 8.8.3)
RPT Assessment Level (% of NBV) (Annex A.26) | Calculated | A = B | All cases: 80% |  |  |  |  | Local Government Code (Annex A.26)
Local Business Tax (Sec. 8.8.3) | Calculated | A = B | All cases: 1% |  |  |  |  | Local Government Code (draft GAIR Sec. 8.8.3)
Government Share (Sec. 8.8.3) | Calculated | A = B | All cases: 0% |  |  |  |  | Not applicable to gas (draft GAIR Sec. 8.8.3)
ER 1-94 host-community benefit (USD/kWh) (Sec. 8.8.3) (US$/kWh) | Calculated | A = B | All cases: 0.00048 |  |  |  |  | PhP 0.03/kWh converted at the model exchange rate
Notes: Taxes and incentives. No BOI or PEZA incentive and no tax holiday. Income tax 25 percent; property tax, local business tax, ER 1-94, and taxes on financing are all included.

## Slide 30: 7. Taxes and incentives (2 of 2)
Parameter | Type | Case | Lot 1 existing | Lot 2 existing | New CCGT | New OCGT | New gas engine | Basis / source
Withholding Tax on Interest (Foreign Currency) - WHT | Calculated | A = B | All cases: 10% |  |  |  |  | NIRC, on foreign-currency interest
Gross Receipts Tax on Interest (Local Currency) - GRT | Calculated | A = B | All cases: 1% |  |  |  |  | NIRC, on local-currency interest
Documentary Stamps Tax (DST) | Calculated | A = B | All cases: 0.5% |  |  |  |  | NIRC, on loan documents
PEZA Incentives (% of gross income) - 0% / 5% | Calculated | A = B | All cases: 0% |  |  |  |  | Calculated by the model
VAT on importation | Calculated | A = B | All cases: 12% |  |  |  |  | 12% VAT (NIRC Sec. 107); see VAT recovery below
Customs Duty | Calculated | A = B | All cases: 3% |  |  |  |  | ERC model default (Annex A.22)
VAT Recovery, % | Calculated | A = B | All cases: 0% |  |  |  |  | 0%: the 70% recovery applies only under a BOI incentive, which is not assumed
Timing of VAT recovery (yrs after COD) | Calculated | A = B | All cases: 0 |  |  |  |  | Not applicable: no VAT recovery assumed
Notes: Continuing this group. Same layout: the value for each case, then the basis. I will pause on any line you flag.

## Slide 31: 8. Economic, working capital and currency (1 of 2)
Parameter | Type | Case | Lot 1 existing | Lot 2 existing | New CCGT | New OCGT | New gas engine | Basis / source
Base Foreign Exchange Rate (US$/US$) - 2028 | Input | A = B | All cases: 1 |  |  |  |  | ERC model default
Forward Fixed Exchange Rate (2028) | Input | A = B | All cases: 1 |  |  |  |  | ERC model default
Base Local CPI - 2028 | Input | A = B | All cases: 160 |  |  |  |  | ERC model default
Annual Local CPI - for OPEX (% p.a.) | Input | A = B | All cases: 0% |  |  |  |  | Real terms: the GAT Price is not indexed (draft GAIR Sec. 8.9)
Annual US CPI - for OPEX (% p.a.) | Input | A = B | All cases: 0% |  |  |  |  | Real terms (draft GAIR Sec. 8.9)
Notes: Economic and currency. Real terms: zero CPI and zero peso depreciation, because the GAT Price is fixed in pesos and not indexed. The exchange rate is the BSP rate of 25 September 2026. Working capital runs on 30 days.

## Slide 32: 8. Economic, working capital and currency (2 of 2)
Parameter | Type | Case | Lot 1 existing | Lot 2 existing | New CCGT | New OCGT | New gas engine | Basis / source
Annual Peso Depreciation Rate (% p.a.) | Calculated | A = B | All cases: 0% |  |  |  |  | Real terms (draft GAIR Sec. 8.9)
Days Receivable, Payable and Inventory (days) | Input | A = B | All cases: 30 |  |  |  |  | ERC model default
PhP per USD exchange rate (Annex A.16) (PhP/US$) | Input | A = B | All cases: 62.756 |  |  |  |  | BSP reference rate, 25 Sep 2026 (Annex A.16)
ER 1-94 benefit, PhP/kWh (Sec. 8.8.3) | Input | A = B | All cases: 0.03 |  |  |  |  | DOE DC2025-10-0023 (draft GAIR Sec. 8.8.3)
Salvage received in last year (1 = yes) (Sec. 8.3) | Input | A = B | All cases: 1 |  |  |  |  | Draft GAIR Sec. 8.3; Annex A.23
Notes: Continuing this group. Same layout: the value for each case, then the basis. I will pause on any line you flag.

## Slide 33: 9. Fuel and technical
Parameter | Type | Case | Lot 1 existing | Lot 2 existing | New CCGT | New OCGT | New gas engine | Basis / source
Fuel switch (fuel is outside the GAT Price) (Sec. 8.6) | Input | A = B | All cases: 0 |  |  |  |  | Fuel is outside the GAT Price (draft GAIR Sec. 8.6)
Gross Heating Value (Btu/lb) | Input | A = B | All cases: 22,129 |  |  |  |  | Natural gas; for the efficiency calculation only
Plant Thermal Efficiency, % | Calculated | A = B | 53.73% | 53.73% | 55.94% | 34.82% | 42.65% | Calculated by the model
Energy conversion constant (model line “Plant Heat Rate”) (kJ/kWh) | Calculated | A = B | All cases: 3,600 |  |  |  |  | 3,600 kJ = 1 kWh. A unit constant, not the Annex A.15 Heat Rate Cap
Fuel Rate (kWh/MT) | Calculated | A = B | 7,683 | 7,683 | 7,998 | 4,978 | 6,098 | Calculated by the model
Lube oil density (kg/L) | Input | A = B | All cases: 0.98 |  |  |  |  | ERC model default
Specific lube oil consumption (g/kWh) | Input | A = B | All cases: 5.4 |  |  |  |  | ERC model default
Lube oil cost (US$/L) | Input | A = B | All cases: 0 |  |  |  |  | ERC model default
Notes: Fuel and technical. Fuel is switched off in the model because it sits outside the GAT Price. These lines remain for the efficiency calculation only and do not affect the GAT Price.

## Slide 34: Visayas cases: values that differ from Luzon (1 of 4)
Parameter | Case | Visayas 440 MW (2028) |  |  | Visayas 500 MW (2031) |  | 
 |  | CCGT | OCGT | Gas engine | CCGT | OCGT | Gas engine
Unit Capacity of Plant (MW/unit) | A = B | 440 | 220 | 22 | 500 | 250 | 25
No. of Units (unit) | A = B | 1 | 2 | 20 | 1 | 2 | 20
Installed Capacity, gross (MW) (Annex A.1) | A = B | 440 | 440 | 440 | 500 | 500 | 500
Net Electrical Output (GWh, first year) | A | 1,618.8 | 1,618.8 | 1,618.8 | 1,839.6 | 1,839.6 | 1,839.6
 | B | 2,433.1 | 2,433.1 | 2,433.1 | 2,764.8 | 2,764.8 | 2,764.8
EPC Cost (US$/kW) | A = B | 946.5 | 568.3 | 907.4 | 946.7 | 568.5 | 907.6
Plant Cost (Excluding VAT, Financing, Working Capital) (US$/kW) | A = B | 1,159 | 697.1 | 1,112 | 1,159 | 697.1 | 1,112
Equipment Cost ex BOP, Transport ($000/MW) | A = B | 754 | 453 | 723 | 754 | 453 | 723
Same per-kW inputs, financing, taxes and timing as new-build Luzon. Case B uses the MERALCO-supplier (Luzon) fleet history. Mindanao: no lot in the DOE TOR.
Notes: These are the only lines where the Visayas cases differ from new-build Luzon: plant size, and the amounts that scale with it. Orange is Visayas 440 megawatts from 2028, magenta is Visayas 500 megawatts from 2031. Per-kW inputs, financing, taxes and timing are the same as Luzon, so the basis column on the earlier slides applies.

## Slide 35: Visayas cases: values that differ from Luzon (2 of 4)
Parameter | Case | Visayas 440 MW (2028) |  |  | Visayas 500 MW (2031) |  | 
 |  | CCGT | OCGT | Gas engine | CCGT | OCGT | Gas engine
EPC (Equipment, Balance of Plant, Transport) (US$ million) | A = B | 416.4 | 250.1 | 399.2 | 473.3 | 284.3 | 453.8
Development & Other Costs (Civil Works, Customs Duty) (US$ million) | A = B | 73.7 | 44.3 | 70.7 | 83.7 | 50.4 | 80.3
Construction Contingency (US$ million) | A = B | 19.2 | 11.5 | 18.4 | 21.8 | 13.1 | 20.9
Value Added Tax (US$ million) | A = B | 36.3 | 21.8 | 34.8 | 41.2 | 24.8 | 39.5
Financing Costs (US$ million) | A = B | 67.6 | 28.8 | 37.0 | 76.8 | 32.7 | 42.0
Initial Working Capital (US$ million) | A = B | 45.9 | 27.6 | 44.0 | 52.2 | 31.4 | 50.1
Total Uses of Fund (US$ million) | A = B | 660.0 | 385.0 | 605.0 | 750.0 | 437.5 | 687.5
Debt (US$ million) | A = B | 462.0 | 269.5 | 423.5 | 525.0 | 306.3 | 481.3
Equity (US$ million) | A = B | 198.0 | 115.5 | 181.5 | 225.0 | 131.3 | 206.3
Same per-kW inputs, financing, taxes and timing as new-build Luzon. Case B uses the MERALCO-supplier (Luzon) fleet history. Mindanao: no lot in the DOE TOR.
Notes: Continuing the Visayas lines. Same colours: orange for 440 megawatts, magenta for 500.

## Slide 36: Visayas cases: values that differ from Luzon (3 of 4)
Parameter | Case | Visayas 440 MW (2028) |  |  | Visayas 500 MW (2031) |  | 
 |  | CCGT | OCGT | Gas engine | CCGT | OCGT | Gas engine
Total Sources of Fund (US$ million) | A = B | 660.0 | 385.0 | 605.0 | 750.0 | 437.5 | 687.5
Fixed O&M Costs ($000/unit/year) (Annex A.4) | A = B | 6,032 | 1,870 | 363 | 6,855 | 2,125 | 412
G&A Costs ($000/year) (Annex A.6) | A | 556 | 661 | 805 | 632 | 752 | 914
 | B | 654 | 881 | 990 | 743 | 1,002 | 1,125
O&M + Spares as % of EPC, T/L, S/S | A | 2.22% | 4.39% | 3.35% | 2.22% | 4.39% | 3.35%
 | B | 2.61% | 5.85% | 4.13% | 2.61% | 5.85% | 4.13%
Local Capital | A = B | 48.98% | 49.05% | 48.99% | 48.97% | 49.03% | 48.98%
Foreign Capital | A = B | 51.02% | 50.95% | 51.01% | 51.03% | 50.97% | 51.02%
Total Local Debt (US$ million) | A = B | 125.3 | 73.3 | 114.9 | 142.3 | 83.2 | 130.5
Total Foreign Debt (US$ million) | A = B | 336.7 | 196.2 | 308.6 | 382.7 | 223.0 | 350.8
Same per-kW inputs, financing, taxes and timing as new-build Luzon. Case B uses the MERALCO-supplier (Luzon) fleet history. Mindanao: no lot in the DOE TOR.
Notes: Continuing the Visayas lines. Same colours: orange for 440 megawatts, magenta for 500.

## Slide 37: Visayas cases: values that differ from Luzon (4 of 4)
Parameter | Case | Visayas 440 MW (2028) |  |  | Visayas 500 MW (2031) |  | 
 |  | CCGT | OCGT | Gas engine | CCGT | OCGT | Gas engine
Total Debt Amount (US$ million) | A = B | 462.0 | 269.5 | 423.5 | 525.0 | 306.3 | 481.3
Equity Investment (US$ million) | A = B | 198.0 | 115.5 | 181.5 | 225.0 | 131.3 | 206.3
Same per-kW inputs, financing, taxes and timing as new-build Luzon. Case B uses the MERALCO-supplier (Luzon) fleet history. Mindanao: no lot in the DOE TOR.
Notes: Continuing the Visayas lines. Same colours: orange for 440 megawatts, magenta for 500.

## Slide 38: Questions for discussion
All-in project cost
Do US$1,500 / 1,375 / 875 per kW (new) and US$600 (existing) match your recent EPC quotes?
Capacity factor
Is 42% (TOR) or the historical 63%–67% the better reference?
O&M
Do the fixed and variable O&M values match current service agreements?
Financing
Are 8% debt, 15-year tenor and 14% equity return achievable today?
Notes: Now we open the floor. These are the four areas where your evidence helps us most. Please raise your hand in the platform; state your company once and keep each point to about two minutes. We will note every point in the comments matrix.

## Slide 39: Next steps
Today
Discussion of model assumptions
Written comments
With evidence, via the Case No. 2026-015 RM docket, by the date in the FGD notice
ERC review
Comments considered in the Reference Parameters
Resolution
Commission issues the GAT Price by resolution
Notes: To close: please send written comments, with supporting documents, through the ERC docket for Case No. 2026-015 RM by the deadline in the FGD notice. We will consider them before the Commission issues the Reference Parameters and the GAT Price by resolution. Thank you for your time.